PowerPoint-Präsentation
 SmartMug
The clever way to order
Martin Dold, Larraitz Orio,
Gürkan Karacocuk, Dennis Tritschler
    Architecture
Android App: Connects to the SmartMug
Wifi access: Wireless Communication
Mug: Standard Mug
Smart Mug: Extension to make your mug smart
Functions
Connection to mug via bar code reading
Liquid level sensing via weight (HX711 circuit)
Drinking statistic analysis via app
Interactive drinking games via app
Waitress communication by changing mug color
        SmartMug
        SmartMug App
HX711
Connect to your
SmartMug via Bar Code
or by entering
manuell the IP Adress
Bayonet mount
Load cell
Display some
statistics like promile
Adafruit Huzzah
RGB-LED
Batteries
Enter your personal Data
for some statistics
Order via SmartMug
Case
Play some drinking
games
        Connection
SmartMug Protocol
TCP/IP → Wireless LAN according to
  IEEE802.11b/g standard
Multicast DNS:
        Service name: smartmug
        Service type: _smartmug._tcp
        Sequence diagram
Tag / 1byte	Length / 1byte	Value / n bytes	End of Frame / 1 byte
More Details under:
https://github.com/martin-dold/smartMug
        Outlook
- Connection to the barkeeper → Live data for the barkeeper, direct re-order function
- Payment via app
- Capacitive measurement instead of weight
- Connection between taps and SmartMug for automated and exact measurement of the filling level