## Slide 1: SmartMug The clever way to order
SmartMug
Martin Dold, Larraitz Orio,
Gürkan Karacocuk, Dennis Tritschler
SmartMug App
Connection
SmartMug Protocol
TCP/IP → Wireless LAN according to
IEEE802.11b/g standard
Multicast DNS:
Service name: smartmug
Service type: _smartmug._tcp
Sequence diagram
Outlook
- Connection to the barkeeper → Live data for the barkeeper, direct re-order function
- Payment via app
- Capacitive measurement instead of weight
- Connection between taps and SmartMug for automated and exact measurement of the filling level
Architecture
Andriod App: Connects to the SmartMug
Wifi access: Wireless Communication
Mug: Standard Mug
Smart mug: Extension to make your mug smart
Functions
Connection to mug via bar code reading
Liquid level sensing via weight (HX711 circuit)
Drinking statistic analysis via app
Interactive drinking games via app
Waitress communication by changing mug color
Connect to your
SmartMug via Bar Code
or by entering
manuell the IP Adress
Order via SmartMug
Play some drinking
games
Display some
statistics like promile
Enter your personal Data
for some statistics
Bayonet mount
Load cell
HX711
Adafruit Huzzah
Batteries
RGB-LED
Case
More Details under:
https://github.com/martin-dold/smartMug
Tag 1byte | Length 1byte | Value n bytes | End of Frame 1 byte